## Thiele Small Parameters

| Re | 3.7 Ohm |
| --- | --- |
| Le | 2.82 mH |
| Fs | 27 Hz |
| Qms | 3.2 |
| Qes | 0.52 |
| Qts | 0.45 |
| Sd | 510 cm ² |
| Vas | 68 L |
| Cms | 0.19 mm / N |
| Mms | 185 g |
| Rms | 10.7 kg / s |
| B * L | 14.5 N / A |
| Sensitivity 1W / 1 m | 86 dB |
| Sensitivity 2.83 V / 1 m | 89.5 dB |

Voice coil data

| Diameter | 50 mm |
| --- | --- |
| Height of winding | 40 mm |
| Support material | Aluminum |
| Coil material | Copper round wire |
| Air gap depth | 24 mm |
| linear excursion Xmax | 16 mm (peak to peak) |
| Outer diameter | 315 mm |
| Mounting diameter | 281 mm |
| Cutting depth, rim height | 12 mm |
| Depth | 158 mm |
| Nominal impedance | 4 Ohm |

## General data and characteristics

- Druckgußkorb black aluminum, very stable against steel basket

- Pole piece for 22 mm voice coil ventilation

- Very stable quality (real) glass fiber honeycomb sandwich membrane (Honeycombwoven) with hard plastic dust cover

- High quality butyl rubber surround for long life

- Large Doppelferritkernmagnetantrieb

- Gold plated terminals for cables up to 10 mm ²

- Very high quality bonds

- Very high loads