## Thiele Small Parameters

| Re | 6.58 Ohm |
| --- | --- |
| Le | 0.4 mH |
| Fs | 58.5 Hz |
| Qms | 2.7 |
| Qes | 0.71 |
| Qts | 0.56 |
| Sd | 70 cm ² |
| Vas | 5.64 L |
| Cms | 0.82 mm / N |
| Mms | 9.03 g |
| Rms | 1.23 kg / s |
| B * L | 5.64 N / A |
| Sensitivity 1 W / 1 m | 86.7 dB |
| Sensitivity 2.83 V / 1 m | 87.6 dB |

## Voice coil data

| Diameter | 25 mm |
| --- | --- |
| Height of winding | 9 mm |
| Support material | Aluminum |
| Coil material | Copper round wire |
| Air gap depth | 5 mm |
| linear excursion Xmax | 4 mm (peak to peak) |
| Outer diameter | 140 mm |
| Mounting diameter | 114 mm |
| Cutting depth, rim height | 4.2 mm |
| Depth | 54 mm |
| Nominal impedance | 8 Ohm |

## General data and characteristics

- Druckgußkorb black aluminum, very stable against steel basket

- 8 mm pole piece for voice coil ventilation

- Very high quality coated paper cone in black unpressed Paper Cone Design

- Inverted dust cap

- High quality butyl rubber surround for long life

- Large Ferritkernmagnetantrieb

- Gold plated solder tails

- Very high quality bonds