Specifications

- OD 109.8 mm

- Mounting diameter 77 mm (without solder tags)

- Mounting depth 40 mm

- Bolt circle diameter 95.6 mm

- Bore holes 6 pieces

- Bore diameter 3.9 mm

- Hole pitch 60 degrees

- Weight 700 grams

- Voice Coil Diameter 28 mm

- Range 2200 Hz-20000 Hz

- Nominal impedance 8 ohms / RDC 6.5 ohms

- Recommended filter circuit 12 dB from 2500 Hz

- Black plastic front

- Vaporised almost transparent silk dome

- Solder tails

- Very high quality bonds

- Voice coil cooled with 7 holes

- Magnetically shielded chassis