## Thiele Small Parameters

| Re | 3.2 Ohm |
| --- | --- |
| Le | 0.24 mH |
| Fs | 55 Hz |
| Qms | 2.8 |
| Qes | 0.67 |
| Qts | 0.54 |
| Sd | 131 cm ² |
| Vas | 15 L |
| Cms | 0.63 mm / N |
| Mms | 10.5 g |
| Rms | 1.5 kg / s |
| B * L | 4.4 N / A |
| Sensitivity 1 W / 1 m | 89 dB |
| Sensitivity 2.83 V / 1 m | 93 dB |

Voice coil data

| Diameter | 25 mm |
| --- | --- |
| Height of winding | 10 mm |
| Support material | Aluminum |
| Coil material | Copper round wire |
| Air gap depth | 6 mm |
| linear excursion Xmax | 4 mm (peak to peak) |
| Outer diameter | 168 mm |
| Mounting diameter | 141 mm |
| Cutting depth, rim height | 4 mm |
| Depth | 66 mm |
| Nominal impedance | 4 Ohm |

## General data and characteristics

- Druckgußkorb black aluminum, very stable against steel basket

- 8 mm pole piece for voice coil ventilation

- Very high quality fiberglass honeycomb sandwich membrane (Honeycombwoven) with hard plastic dust cover in phase plug design

- High-quality butyl rubber surround for long life

- Large Ferritkernmagnetantrieb

- Gold plated solder tails

- Very high quality bonds