### Thiele/Small Parameters

| Re | 6.54 Ohm |
| --- | --- |
| Le | 0.56 mH |
| Fs | 26.8 Hz |
| Qms | 1.98 |
| Qes | 0.46 |
| Qts | 0.37 |
| Sd | 216 cm ² |
| Vas | 115 L |
| Cms | 1.76 mm / N |
| Mms | 20 g |
| Rms | 1.85 kg / s |
| B * L | 6.64 N / A |
| Sensitivity 1 W / 1 m | 88.7 dB |
| Sensitivity 2.83 V / 1 m | 89.6 dB |

Voice coil data

| Diameter | 35 mm |
| --- | --- |
| Height of winding | 15 mm |
| Support material | Aluminum or ASV (high temperature resistant) |
| Coil material | Copper round wire |
| Air gap depth | 6 mm |
| linear excursion Xmax | 9 mm (peak to peak) |
| Outer diameter | 217 mm |
| Mounting diameter | 188 mm |
| Cutting depth, rim height | 5 mm |
| Depth | 88 mm |
| Nominal impedance | 8 Ohm |

## General data and characteristics

- Druckgußkorb black aluminum, very stable against steel basket

- Pole piece for 15 mm voice coil ventilation

- Very high quality coated paper cone in black unpressed Paper Cone Design

- Inverted dust cap

- High quality butyl rubber surround for long life

- Large Ferritkernmagnetantrieb

- Gold plated solder tails

- Very high quality bonds